## Slide 1: Formulating with Solid Fats: It’s All About Context
By: Gabrielle Scott

## Slide 2: Applications for Solid Fats
All-purpose shortening
Fluid shortenings
Cake shortening
Icing shortening
Filler fat shortenings
Bread shortening
Frying shortening
Pie crust shortening
Pastry shortening
Confectioner’s fat

## Slide 3: Methods for Obtaining Functional Fats
Hydrogenation
Interesterification
Process Control
Crystal Seeding
Additives

## Slide 4: Triglyceride

## Slide 5: Melting points of Fats: The basics
Melting point increases with:
  Chain length
  Saturation
  Even chain FA
  Trans fats 
Shortenings have a melting Range not Melting Point
TAGs can be broken into distinct groups based on melting point and functionality

## Slide 6
Group I
  Provides structure
  Solid at room temp.
Group II
  Structure and lubricity
  Solid at room temp. and liquid at body temp.
Group III and Group IV
  Imparts tenderness and richness
  More unsaturated
Body temperature = 37°C
Room temperature = 20°C

## Slide 7: Plastic fats
Plastic fats are a crystalline network on a continuous oil matrix
Polymorph forms
  alpha (α)
  beta-prime (β’)
  Beta (β)
Thermodynamic stability
α
Β’
Β
Most Functional
Notes: The beta-prime polymorph is usually the most functional in fat products, due to its small crystal size (1mm) and thin, needle shaped morphology.

## Slide 8
Beta-prime-type (β′) | Beta-type (β)
Soybean | Cottonseed
Safflower | Palm
Sunflower | Tallow
Sesame | Milk Fat
Peanut | 
Corn | 
Olive | 
Coconut | 
Palm kernel | 
Lard | 
Cocoa butter | 

## Slide 10: Crystallization
Heterogeneous – impurities, lower activation energy
Homogeneous – rare in shortening/margarine
Steps
Nucleation- Supersaturation and Supercooling
Crystal Growth – low temp
Crystal Ripening – long time

## Slide 11: Process Control
Agitation
  Agitation in the holding tubes prevents crystallization
  Stick margarine vs. tub margarine
Tempering
  Holding for 1-10 days after crystallization begins
  Preferred polymorphic state
  Delays β’  β

## Slide 12: Seeding Crystals
Saturated or Unsaturated TAGs (triacylglycerols)
Seed should have same polymorphic state as desired (β’ or β)
Prevents incomplete crystallization
Reduces temperature sensitivity

## Slide 13: Crystallization Modifiers and Additives
Diacylglycerols (DAGs)
Monoacylglycerols (MAGs)
Sorbitan esters (SE)
Sucrose esters of fatty acids (SEFAs)
Lecithin
Polyglycerol polyricinoleate (PGPR)
Minor Lipids
Emulsifiers

## Slide 14: Retaining β’ Structure
β’  β – Fat Bloom
>2-3% additives will limit β’ formation
Polyglycerol polyricinoleate (PGPR) + Lecithin
  slowing the α→β′→β transitions
Diacylglycerols (DAGs)
  Inhibits crystal growth and nucleation
Palm oil prevents conversion of β’ to β
  Less homogeneity of FA chain length

## Slide 15: Applications for Solid Fats
Fluid shortenings  Lecithin inhibits crystallization
Cake shortening  Mono/Di- glycerides form complex with amylose
Icing shortening  β’ stable for smoothness and aeration
Filler fat shortenings  PHOs + emulsifiers for stability
Bread shortening  Solid fat content strengthens dough
Frying shortening  flavor, frying, oxidative stability (context dependent)
Pie crust shortening  NO emulsifiers for non-uniform fat distribution
Pastry shortening  70:30 lard:hydrogenated oil for stability
Confectioner’s fat  TAGs that melt at 32-35°C

## Slide 16: Consumer Education and Expectation
Consumer may not understand why you used that ingredient but that won’t stop them from caring!
Example: Have you ever heard of Rapeseed oil?
  Canola Oil is made from rapeseeds low in erucic acid and glucosinolates.
Can
+
ola
Canadian
Oil

## Slide 17: References
1. Ravotti, R.; Worlitschek, J.; Pulham, C.R.; Stamatiou, A. Triglycerides as Novel Phase-Change Materials: A Review and Assessment of Their Thermal Properties. Molecules (Basel, Switzerland) 2020, 25, 5572.
2. Nguyen, V.; Rimaux, T.; Truong, V.; Dewettinck, K.; Van Bockstaele, F. Granular Crystals in Palm Oil Based Shortening/Margarine: A Review. Crystal growth & design 2020, 20, 1363-1372.
3. Sato, K. Crystallization behaviour of fats and lipids — a review. Chemical engineering science 2001, 56, 2255-2265.
4. Wiedermann, L.H. Margarine and margarine oil, formulation and control. Journal of the American Oil Chemists' Society 1978, 55, 823-829.
5. Ribeiro, A.; Ribeiro, A.; Masuchi, M.; Masuchi, M.; Miyasaki, E.; Miyasaki, E.; Domingues, M.; Domingues, M.; Stroppa, V.; Stroppa, V.; de Oliveira, G.; de Oliveira, G.; Kieckbusch, T.; Kieckbusch, T. Crystallization modifiers in lipid systems. J Food Sci Technol 2015, 52, 3925-3946.
6. GHOTRA, B.S.; DYAL, S.D.; NARINE, S.S. Lipid shortenings: a review. Food research international 2002, 35, 1015-1048.